## Slide 1
ניתוח, עיבוד ומידול של צעדים
מתוך נתוני דגימות של מדי תאוצה
IMU
Accelerometers Step Modeling
Name: Omri Weiss
Id: 308248657

## Slide 2: Task
6 Steps of Analyzing Data
.h5 Files given,
containing
Data Samples(double numbers)
to analyze and
calculate
I Chose this file
To work with

## Slide 3: General Data Explain

## Slide 4: First Step
Which Samples belong to the height acceleration?!
All blue marked rows
Are ≈ -9.8 m/
Which is the gravity of earth acceleration (denoted by G) downwards, acting on the foot measured at the height axis.
Therefore we will not use them to analyze steps.
.h5 data presented as text

## Slide 5
So we are using the 2nd rows, determining by their numbers where each step of the walk begins and where it ends.
We will call this data Width, because the width changes less than the length axis during the walk.

## Slide 6
The width samples are a ‘data value’ in Matlab.
And each step we need to separate is a ‘data sample’ in Matlab :
The whole IMU Accelerometer data in .h5 is called ‘timeseries Object’ :
Concepts
The specific time here: 37,713
Data Sample time here: 7,680
Number of Data Samples: 5

## Slide 7: Dividing steps visually
As I was plotting the width samples on screen,
I noticed there are 5 ‘chunks’= Steps in this Movement Data
(marked in Red).
Each of their size
was defined in data as: 7680
5 * 7680 = 38,400 ≈ 37,713

## Slide 8: Step 2:removing abnormal steps
Using High Pass Filter(HPF) Function as done in course, I filtered out these abnormal noises:
Resets all signals that
are not within frequencies
range of |c|

## Slide 9: Step 3: Median signal pattern
We use median function(as practiced in lectures) on each one of the 3 Axises we got:
Median Filter function:

## Slide 10: Step 4:Calculating Percentiles
What is a Percentile?
Percentile is a value below which a certain percentage of observations lie.
Percentile 10 is a number that under it there are 10% of the samples in the data.
It doesn’t have to be one of the data samples(like in this case).
Prctile is a Matlab Built-in Function:
I Used it with values 10 and 90:

## Slide 11: Step 5:Interpolation
Interpolation Is used for adding new data points within a range, in this case it is 3 Dimensions data points.
3D
Given Points
to interpolate to
2D
Given Points to interpolate to

## Slide 12: Step 5:Interpolation
אוסף הדגימות הנתון
למשל -
Height Acceleration
לא הכרחי,שדה שמציין
שיטת אינטרפולציה חלופית לשיטת ברירת המחדל
משתנה שמכיל את הדגימות שאנחנו רוצים לקרב אליהן
וקטור דגימות זהה בגודלו ל-
שאליו אנחנו רוצים לקרב את הדגימות החדשות
x
וקטור שמכיל את האחוזונים
10,90 של דגימות תאוצת הגובה
מסוננות לפי
Median Filter
דגימות תאוצת הגובה
מסוננות לפי
Median Filter
Code Implementation:

## Slide 13: Step 6:Plot Graph of Median&Perecentiles
Showing Percentiles over the
Median filtered graphs